## Slide 1: Economic Viability Analysis for a 400MW Windfarm
Mohamad Mostafa Hareb Karim Hamawi
Samir Wadih

## Slide 2: Project Description
Number of MW produced by the entire farm | 400
Number of MW produced by a single turbine | 2
Number of Turbines Needed for the Project | 200
Average Price for a single turbine | 3000000
Price for all Turbines | 600000000
Wind Capacity factor in Marjayoun (Where project will take place) | 0.49
KWh Produced | 1716960000
Per capita KWh consumed | 2292
Per household KWh consumed | 8709.6
Households covered by our project | 197134.197
Number of Households in lebanon | 1266000
Coverage of local electric demand by single wind farm | 15.571%

## Slide 3: Cost of Land
Land Cost Estimation | 
Area Needed per turbine (acres) | 1.5
Area Needed per turbine (m^2) | 6070.3089
Total Area needed for turbines(m^2) | 1214061.8
Total Area neededfor turbines(km^2) | 1.2140618
Total area for facilities needed | 10000
Price of 1 m^2 land in Marjayoun | 40
Total areas including facilities | 1224061.8
Price of all the land needed | 48962471

## Slide 4: Total Initial Costs
Construction Costs | 
Price of Turbines with the installation | 600000000
Price of Transportation of Material | 3000000
Facility Building and Miscellaneous costs | 2000000
Powerplant Infrastructure | 2000000
Cost of Labor | 1500000
Planning and Permits | 2000000
Cost Basis (including Land) | 659462471

## Slide 5: Annual O&M Costs
Annual Costs | 
Average O&M costs per turbine | 48000
Average O&M costs for all turbines | 9600000
Labor costs per employee | 20000
Facility running and services | 100000
Labor costs for 200 employees | 4000000
Annual Insurance and Property Taxes(5%) | 2448123.566
Total O & M Annual Costs | 16148123.57

## Slide 6: Bank Loan Details
Total Principal Amount | 459462471.3
K | 12
M | 12
C | 1
N (years) | 25
N (months) | 300

## Slide 7: Bank Loan Details
Years | Monthly Interest | APR
Years 1-5 | 0.250% | 3%
Year 6-10 | 0.292% | 3.50%
Year 11-15 | 0.308% | 3.70%
Year 16-25 | 0.330% | 3.960%

## Slide 8: Loan Payment Details
v

## Slide 9: Principal Balance Left to Pay
Chart: 
Months

## Slide 10: Depreciation (Straight Line)
Depreciation (Standard Line Method) | 
Cost Basis | $659,462,471.32
Total Salvage Value | $99,754,965.58
Depreciable Life in years | 25
Total Annual Depreciation | $22,388,300.23

## Slide 11: Total Depreciation Graph
Chart: 
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25
Book Value | 637074171.089 | 614685870.8596 | 592297570.6301 | 569909270.4007 | 547520970.1712 | 525132669.9418 | 502744369.7123 | 480356069.4829 | 457967769.2534 | 435579469.024 | 413191168.7945 | 390802868.5651 | 368414568.3356 | 346026268.1062 | 323637967.8767 | 301249667.6473 | 278861367.4178 | 256473067.1884 | 234084766.9589 | 211696466.7294 | 189308166.5 | 166919866.2705 | 144531566.0411 | 122143265.8116 | 99754965.5822

## Slide 12: Capital Recovery
MARR= | 10%
Salvage Value for Land(20% increase)= | $ 58,754,965.58
Salvage Value for single turbine= | $ 200,000.00
Salvage Value for all turbines= | $ 40,000,000.00
Facility Salvage Value= | $ 1,000,000.00
Total Salvage Value= | $ 99,754,965.58
Cost Basis Total= | $ 659,462,471.32
CR(MARR=10%)= | $ 71,637,393.46

## Slide 13: Equivalent Annual and Per Unit Costs

## Slide 14: Annual Revenues
Charge per KWH= | $0.08
N | Annual Revenues
0 | 137356800
1 | 137356800
2 | 137356800
3 | 137356800
4 | 137356800
5 | 137356800
6 | 137356800
7 | 137356800
8 | 137356800
9 | 137356800
10 | 137356800

## Slide 15: Net Income Statement

## Slide 16: Cash Flow Statement

## Slide 17: Cashflow Diagram (Revenues and Expenses)

## Slide 18: Net Cash Flow Diagram

## Slide 19: Break-even Point
2.48 years

## Slide 20: Decision Analysis Based on Several Criteria
Criterion | Value | Case | Decision
ROR | 40.09% | ROR>MARR (10%) | Accept
NPV | $480,838,364.07 | NPV>0 | Accept
AEW | $52,973,035.60 | AEW>0 | Accept
Break Even Point | 2.48 Years≈ 2.5 Years | BEP<25 Years | Accept